## Slide 1
Richard Segovia Barreales
Reducing dizziness when using a video-see-through head mounted display
Tutor: Coen Antens
Empresa: Computer Vision Center (CVC)
Treball Final de Grau Enginyeria Informàtica
Curs 2017 - 2018
Tutor: Felipe Lumbreras Ruiz
Departament: Ciències de la Computació
Menció en computació
Despite the great advances , users still feel dizzy when using Head Mounted Devices (HMD) :
Evaluate whether the user correctly perceives distances and sizes of the objects in 3D space.
Evaluate the user experience when using the HMD and determine whether the accommodation-vergence effect causes dizziness.
Develop a system capable of adapting the visualization to the viewed scene, using depth info .
INTRODUCTION
Accommodation vergence conflict:
Occurs when looking at a screen that is close to the eyes.
Caused by the difference between accommodation distance and vergence distance.
Size issue:
Objects on the screen seem to be at different distances and have different sizes than the objects in the real world.
Caused by the difference between the position of the eyes and the position of the cameras.
PROBLEM
PIPELINE
During the project a tool was developed to dynamically change the visualization settings.
Users felt that the software improves their user experience when using video-see-through devices
Future work
Depth map information can be used in AR applications.
Use Depth info to apply DoF blur in areas where the image cannot be not fused by the eye to reduce Accommodation Vergence conflict.
CONCLUSION
A video-see-through prototype developed at the CVC was used in this project.
The depth map is generated using the images from two cameras on a stereo matcher.
PROTOTYPE
Left
Right
RECTIFICATION
DEPTH MAP
PROCESS
CLASSIFY DISTANCE
CHANGE THE VISUALIZATION
SETTING
USER SETTINGS
Users are able to determine one visualization setting for each distance. After two user testing sessions, one observed the following:
Users prefer a specific setting for a specific viewing distance.
Users do not feel comfortable using settings that belong to other distances.
The same thing happens when applying zoom to the image.
THREAD ARCHITECTURE
Grabbing
Thread 1
Grabbing
Thread 2
Left
Camera
Right
Camera
Grabs lastest image
Grabs lastest image
Grabs
image pair
Classification
value
Displaying Thread
Displaying
ROI
Preset
transition
Processing Thread
Undistort
LIBELAS
Classification